# Bio-Plex Multiplex Phosphoprotein Assay Protocol Outline

# For full instructions see BioPlex Binder or the protocol online at BioRad.com

# Bring all buffers and diluents to room temp prior to use.  Turn on the Bio-Plex instrument 1 hour prior to plate reading.

PREPARE BEADS

- Determine the total number of wells that will be required.

  - As a precaution, add 2 extra wells for every 8 wells actually required..

- Vortex the anti-phosphoprotein bead (50x) stock solution at medium speed for 30 sec.

- Prepare a 50 fold working dilution of the anti-phosphoprotein bead (50x) stock solution in Bio-Plex phosphoprotein wash buffer.

  - Document all volume calculations.

  - Protect the beads from light.

  - Keep all bead solutions on ice when not in use

# PREPARE CONTROL AND SAMPLE CELL LYSATES

- Thaw positive and negative control and sample cell lysates on ice.  Lysates should be diluted to target concentration in lysis buffer, then diluted 1:1 with Bio-Plex assay buffer. Recommend making 120uL of this 1:1 dilution per sample to spot duplicate wells.

# ASSAY

- Cover all unneeded wells with plastic adhesive plate sealer.

- Set the vacuum pressure to 2 inches Hg using a standard flat bottom 96-well plate. Check before each vacuum filtration step to prevent damaging filter plate.

- Pre-wet the filter plate with 100 l of Bio-Plex phosphoprotein wash buffer.

- Vacuum filter. Blot the bottom of plate after this and every vacuum filtration.

- Add Beads.

  - Vortex the working Bead solution at medium speed for 30 sec and add 50 l to each well.

- Vacuum filter.

- Filter wash 2X with 100 l Bio-Plex phosphoprotein wash buffer.

- Add positive and negative controls.

  - Vortex for 5 sec and immediately add 50 l to the appropriate wells.

  - Remember to also include the appropriate blanks (lysis buffer)

- Add samples.

  - Vortex for 5 sec and immediately add 50 l to the appropriate wells.

- Cover the wells with plastic adhesive plate sealer, and blot the bottom of the plate.

- Cover with foil and incubate overnight at room temp with shaking.

  - Slowly ramp up to 1,100 rpm and shake at high speed for 30 sec

  - Reduce speed to 300 rpm for the remainder of incubation

PREPARE DETECTION ANTIBODY (DURING PRECEEDING INCUBATION AND 10 MIN PRIOR TO USE)

- Determine the total number of well that will be required.

  - As a precaution, add 2 extra wells for every 8 wells actually required.

- GENTLY VORTEX the multiplex detection antibody (25x) stock solution.

- Prepare a 25 fold working dilution of the detection antibody (25x) stock solution in Bio-Plex phosphoprotein detection antibody diluent.

  - Document all volume calculations.

  - Protect the antibody from light.

  - Keep all antibody solutions on ice when not in use.

- Remove the plate sealer and filter wash 3X with 100 l Bio-Plex phosphoprotein wash buffer.

- Gently vortex the detection antibody and add 25 ul to each well.

- Cover the wells with plastic adhesive plate sealer, and blot the bottom of the plate.

- Cover with foil and incubate for 30 min at room temperature with shaking.

  - Slowly ramp up to 1,100 rpm and shake at high speed for 30 sec

  - Reduce speed to 300 rpm for the remainder of incubation

PREPARE STREPTAVIDIN-PE (DURING PRECEEDING INCUBATION AND 10 MIN PRIOR TO USE)

- Determine the total number of wells that will be required.

  - As a precaution, add 2 extra wells for every 8 wells actually required.

- Vigorously vortex the Streptavidin-PE (100x) stock solution.

- Prepare a 100 fold working dilution of the Streptavidin-PE (100x) stock solution in in Bio-Plex phosphoprotein wash buffer.

  - Document all volume calculations.

  - Protect the solution from light.

  - Keep on ice when not in use

- Remove the plate sealer and filter wash 3X with 100 l Bio-Plex phosphoprotein wash buffer.

- Vortex the streptavidin-PE working dilution and add 50 l to each well.

- Cover the wells with plastic adhesive plate sealer, and blot the bottom of the plate.

- Cover with foil and incubate for 10 min at room temperature with shaking.

  - Slowly ramp up to 1,100 rpm and shake at high speed for 30 sec

  - Reduce speed to 300 rpm for the remainder of incubation

- Remove the plate sealer and filter wash 3X with 100 l Bio-Plex phosphoprotein wash buffer

- Resuspend the beads in each well with 125 l of Bio-Plex bead resuspension buffer B.

- Cover the wells with plastic adhesive plate sealer, and thoroughly blot the bottom of the plate.

- Shake the plate at 1,100 rpm for 30 sec – slowly ramp up to this high speed

- Remove the sealer and read the plate.

NOTE:  Set the Bio-Plex Reader to read only 25 beads/region in a volume of 50 uL

Bio-Plex Multiplex PhosphoproteinAssay Dilution Worksheet

# of required wells ______

# of extra wells      ______ (2 wells for every 8 required wells)

_______ total number of wells for dilution calculations

# Bead Dilution

50 l/well

1 l of bead (50x) stock solution/well

________ x 2 l = _______ of bead (50x) stock solution (assay module)

________ x 48 l = ______ of Bio-Plex Phosphoprotein Wash Buffer (phosphoprotein 				reagent kit)

________ x 50 l = ______ total volume

# Detection Antibody Dilution

25 l/well

1 l of detection antibody (25x) stock solution/well

________ x 1 l = _______ of detection Ab (25x) stock solution (assay module)

________ x 24 l = ______  of Bio-Plex Detection Ab Diluent A (phosphoprotein 				reagent kit)

________ x 25 l = ______ total volume

# Streptavidin-PE Dilution

50 l/well

0.5 l of streptavidin-PE (100x) stock solution/well

________ x 0.5 l = _______ of streptavidin-PE (100x) stock solution (phosphoprotein 				reagent kit)

________ x 49.5 l = ______ of Bio-Plex Phosphoprotein wash buffer 						(phosphoprotein reagent kit)

________ x 50 l = ______ total volume